## Slide 1: CSE 4615:: Wireless Networks
Lecture 8.2
Content Contributors:
Course Teacher:
Ashraful Alam Khan
Assistant Professor, CSE, IUT
Understanding Vehicular Communication
Christoph Sommer and Falko Dressler
Cambridge University
Johan J. Lukkien
TU/e Informatica, System Architecture and Networking

## Slide 2: Course Material
Book design © 2014 Cambridge University Press
Title | Vehicular Networking
Authors | Christoph Sommer and Falko Dressler
Publisher | Cambridge University Press
Date | December 2014
Format | Hardback (also available as eBook)
ISBN-10 | 1107046718
ISBN-13 | 9781107046719
Website | http://book.car2x.org

## Slide 3: Vehicular Networking
Book design © 2014 Cambridge University Press

## Slide 4: About this slide deck
These slides are designed to accompany a lecture based on the textbook “Vehicular Networking” by Christoph Sommer and Falko Dressler, published in December 2014 by Cambridge University Press.
Except where otherwise noted (e.g., logos and cited works) this slide deck is Copyright © 2009-2015 Christoph Sommer, but made available to you under a Creative Commons Attribution-ShareAlike 4.0 International License.
In brief, this means you can share and adapt the slides as long as you follow the terms set out in this license [1]. If you split this slide deck into multiple parts, make sure to include appropriate attribution in each part.
This slide deck would not have been possible without the contributions of Falko Dressler, David Eckhoff, Reinhard German, and Kai-Steffen Jens Hielscher.
Please leave this slide intact, but indicate modifications below.
  Version 2015-02
    Improved version for release on book website (Christoph Sommer)
Updated versions of the original slide deck are available online [2].
[1] http://creativecommons.org/licenses/by-sa/4.0/
[2] http://book.car2x.org/

## Slide 5: A Short Introduction
…to Vehicular Networking
                Illustration © 2010 Christoph Sommer

## Slide 6: Introduction of VANET
Vehicular Ad-Hoc Network or VANET is an application of MANET that uses moving vehicles as nodes to create a mobile network [1].
Fig. 1. Types of Networks

## Slide 7: Cont…
VANET turns every participating vehicle into a wireless router or node, allowing vehicles approximately 300m to 1 km of each other to connect and, in turn, create a network with a wide range.
VANET enables communication among the vehicles and roadside infrastructures. It makes transportation systems more intelligent. Since the movement of vehicles are restricted by roads, traffic regulations we can deploy fixed infrastructure at critical locations [2].
The primary goal of VANET is to provide road safety measures where information about vehicle’s current speed, location coordinates are passed with or without the deployment of infrastructure. Apart from safety measures, VANET also provides value added services like email, audio/video sharing etc [3].
The best example of VANET is Transport System of any travel agency or any company which is joined internally.

## Slide 8: Components of VANET
The major components of a VANET are :
  On-Board Unit (OBU)
  Road Side Unit (RSU)
  Trusted Authority (TA)
Fig. 2. VANET Architecture[4]

## Slide 9: Cont…
OBUs are installed in vehicles to provide wireless communication capability.
While RSUs are deployed on intersections or hotspots as an infrastructure to provide information or access to the Internet for vehicles within their radio coverage.
The AS is responsible for installing the secure parameters in the OBU to authenticate the user

## Slide 10: Cont…
DSRC (Dedicated Short Range Communications), WAVE (Wireless Access in Vehicular Environments) or even IEEE 802.11p are used to designate the entire protocol stack of standards dealing with VANETs.
An intelligent vehicle as it was designed in incorporates basically a set of sensors (front radar, reversing radar, etc.) that receive useful environmental information that generally the driver alone is unable to perceive. We find also a positioning system such as GPS (Global Positioning System) for example, which is essential for locating and driving assistance. A smart vehicle is obviously equipped with a communication system (can be multi-interface), a computing system, an event recording device which is a device whose functioning is similar to the black box of an aircraft.
Mainly, and for security measures, a smart vehicle must be equipped with an ELP (Electronic License Plate) or with ECN (Electronic Chassis Number) which represent the electronic identity of the vehicle instead of the conventional identification by license plates. The ITS current terminology includes some features such as transceiving, display and interactivity with the driver in a single unit called OBU.

## Slide 11: Smart Vehicle

## Slide 12: Components of VANET
Vehicles
Electronic and hardware components like sensors and actuators, also software components like operating systems, diagnostics software, peripheral drivers and so on.
Intelligent Actuators are five separate main units of the vehicle
  (Engine, Transmission, Suspension, Brake system and Steering system )
Integrated Vehicle Control which has an influence on the movement of the whole vehicle.
Sensor devices
  (Radar, Video Camera, and Lidar “static laser Scanner, in 1 direction”)
Road side Unites.
Control of Vehicle Groups and Fleets

## Slide 13: Vehicles operate using networked ICT
Local
Control
Local
Control
Local
Control
In-car network
Driver
Control

## Slide 14: Vehicles become parts of a larger whole
Vehicle to Vehicle (V2V) communication
  ad-hoc
  collaborative applications
Applications are distributed
Actuation may pass by driver control
Driver
Control
Driver
Control
Driver
Control
V2V network
Accident prevention

## Slide 15: A conceptual view
V2V
V2V
Internet, V2I
Congestion control
Road maintenance
Environment control
End-user applications
Car sharing
Event management
Driver
Control
Driver
Control
V2V network
Accident prevention
Local
Control
Local
Control
Local
Control
In-car network
Driver
Control
(2)
(1)
(4)
(3)
Example data flows:
  (1) gather detailed driving data to determine
    local weather
    road condition
  (2) accident prevention by direct intervention
  (3),(4) informing driver about upcoming road conditions

## Slide 16
Physical organization in V2V
Vehicle
RSU
RSU
RSU
IEEE 802.3, (ethernet) IEEE 802.11 (WiFi)
……
IEEE 802.16e (WiMAX)
3G, 4G
Moving vehicles connect ad-hoc to each other and to access points of the ambient infra structure
Technology: IEEE 802.11p
Road side units (RSUs, network central devices) are connected to the Internet
IP-based network with wide-area coverage, wireless or wired
Vehicle
Vehicle
Vehicle
Vehicle
IEEE 802.11p

## Slide 17: Executive Summary
The Concept
vehicle-to-vehicle (V2V).
The Opportunity
Smart Cars
The Potentials
Safer roads
Less traffic
Less fading

## Slide 18: Visionary Applications
Lane assistant
  Simple roadside beacons support lane detection
Lateral collision avoidance
  More advanced beacons on cars and motorcycles help maintain minimum separation
Accident reporting
  Broken down cars can automatically send simple report to central server
Intersection assistance
  Pairs of cars automatically coordinate complex maneuvers at intersections
Cooperative driving
  The future evolution of autonomous driving: vehicles actively support each other’s route planning, navigating, driving

## Slide 19: Visionary Applications
...and much (much) more:
Emergency Brake Light Warning, Accident Warning, Emergency Flashlights, Traffic Jam Warning, Weather Warning, Emergency Vehicle, Slow Vehicle, Moving and Static Road Works, Obstacle Warning, Intersection Maneuvering Assistance, Intersection Traffic Lights, Lane Change, Maneuvering Assistance, Longitudinal Maneuvering Assistance, Floating Car Data Collection, Free-Flow Tolling, Breakdown Call, Remote Diagnostics, Theft Detection, Emergency Call, Just-In-Time Repair Notification, Roadside Traffic Camera pull, In-vehicle signing pull, Regional Information pull, Car-specific Software Application Download pull, Electronic Payment pull, Logistic for goods being loaded and unloaded, Traffic Information Service pull, Traffic Information Service push, Electronic Payment push, Roadside Traffic Camera push, In-vehicle signing push, Car specific Software Application Download push, Telemetric Onboard/Off-board Diagnostics, Remote Vehicle Status Control, Fleet Management, Server based navigation, Remote lock-down, Remote entry, Mobile Office, Videophone, Personal Data Synchronization at home, General Map Downloads and Updates, Instant Messaging, General internet services, Internet Audio, continuous feed, Web Browsing, Movie rental, Remote Home Activation/Deactivation pull, Remote Home Control pull, Remote Home Activation/Deactivation push, Remote Home Control push, Voice Chat, Games, Electronic Toll Collection, Parking Unit Fee Payment (drive through payment), Goods and services discovery and payment, Guided Tour, Interactive Lights Dimming, Emergency Traffic Light Pre-emption, Traffic Light Assistant, …
Source: C2CCC, Aktiv-AS/VM

## Slide 20: Visionary Applications (Classified)
The aim of VANET is to improve driving experience and the safety of transportation [5].
  1. Safety Application (to enhance driving safety):
    EEBL – Emergency Electronic Brake Light (sudden braking)
    PCN – Post Crash Notification
    RFN – Road Feature Notification (ex. downhill curve)
    LCA – Lane Change Assistance

## Slide 21: Cont…
  2. Convenience Application (for better driving experience):
    Road Congestion Notification
    Dynamic Route/Travel Time Planning
    Finding Parking Spots
  3. Other Commercial/ Infotainment Application:
    Free flow Tolling
    Social Networking
    Multimedia Content Exchange

## Slide 22: C’est le Rush https://www.youtube.com/watch?v=Johmxw3cspA

## Slide 23
from: Vehicle-to-Vehicle Communications: Readiness of V2V Technology for Applications, NHTSA, August 2014

## Slide 24: Some application examples (US WAVE BSM ~SAE J2735)
Apps. | Comm.type | Freq. | Latency | Range
Lane Change Warning | V2V, periodic, P2M | 10Hz | 100ms | 150m
Collision Warning | V2V, periodic, P2M | 10Hz | 100ms | 150m
Emergency Brake Lights | V2V, event-driven, P2M | 10Hz | 100ms | 300m
Pre-Crash Sensing | V2V, event-driven, P2P | 50Hz | 20ms | 50m
Stop Sign Assists | I2V and V2I, periodic | 10Hz | 100ms | 250m
Left Turn Assistance | I2V and V2I, periodic, P2M | 10Hz | 100ms | 300m
Traffic Signal Violation | I2V, periodic, P2M | 10Hz | 100ms | 250m
Curve Speed Warning | I2V, periodic, P2M | 1Hz | 1s | 200m
Eight high priority vehicle safety applications as chosen by NHTSA and VSCC.
NHTSA – US National Highway Traffic Safety Administration
VSCC – Vehicle Safety Communication Consortium of CAMP (Crash Avoidance Metrics Partnership)
V2V = Vehicle to Vehicle
P2M = Point to Multipoint
I2V = Infra structure to Vehicle
Notes: Including road-side warning and Probe data (floating car data)

## Slide 25: Cont…
The Emergency Electronic Brake Light (EEBL) application enables a vehicle to broadcast a self-generated emergency brake event to surrounding vehicles. Upon receiving the event information, the receiving vehicle determines the relevance of the event and if appropriate provides a warning to the driver in order to avoid a crash. This application is particularly useful when the driver's line of sight is obstructed by other vehicles or bad weather conditions (e.g., fog, heavy rain).
When a vehicle brakes hard, the Emergency Electronic Brake Light application conveys this information to surrounding vehicles via one or more Basic Safety Messages. This application will help the driver of a following vehicle by giving an early notification that the lead vehicle is braking hard even when the driver’s visibility is limited (e.g. a large truck blocks the driver’s view, heavy fog, rain).
The current brake lamp goes on when the driver applies the brake. The Emergency Electronic Brake Light application might not only enhance the range of a hard braking message but also might provide important information such as acceleration/deceleration rate and duration. At present, brake lamps do not differentiate level of deceleration and are only useful as far rearward as line of sight allows.

## Slide 26: Cont…
A Post Collision Notification application detects an incident based on the speed and deceleration of each vehicle or node.
Lane Change Assist (LCA) uses radar sensors to help the driver to monitor the blind-spot area and the traffic situation behind the vehicle. Lane Change Assist measures the closing speed of an approaching vehicle in the adjacent lane to determine if changing lanes is safe and if it’s not, gives the driver an audible and visual warning.
Cooperative Collision Warning (CCW), which provides an active safety mechanism for vehicles on highways, is implemented by exchanging static and dynamic vehicle parameters with neighboring vehicles through inter-vehicle wireless communications. Received information is not only used for calculating the relative safety distance between neighboring vehicles, but also stored in a Motor Vehicle Event Data Recorder (MVEDR) for future accident investigation.

## Slide 27: Cont…
The CCW concept provides warnings or situation awareness displays to drivers based on information about the motions of neighboring vehicles obtained by wireless communications from those vehicles, without use of any ranging sensors. Collision Warning Systems share a common need: the vehicle needs to know about the locations and motions of all the neighboring vehicles, representing the state of the vehicle neighborhood.
Most collision warning systems in the literature try to learn the state of the neighboring vehicles or roadway by using sensors like radar, laser, or vision (1) looking forward, to the rear, to the right lane and left lane. In contrast, our collision warning system develops its knowledge of the vehicle neighborhood by listening to the wireless communications of other vehicles and reciprocates with communications of its own.

## Slide 28: Characteristics
High Mobility
Rapid Changing Network Topology
Predictable Mobility
No Power Criteria
Time Management [6]

## Slide 29: Cont…
VANET is an application of MANET but it has its own distinct characteristics, the characteristics of VANETs are basically a mixture of wireless medium characteristics. The characteristics are:
1. High Mobility: - This is important features of the VANET as nodes move in a high speed all the time with different direction . The high mobility of nodes reduces the mesh in the network (fewer routes between nodes). Compared to MANET, VANET mobility is relatively high.
2. Rapid Changing Network Topology: - As nodes move in very high speed so the position of node changes frequently so therefore network topology in VANETs tends to change frequently. The connection times are short especially between nodes moving in opposite direction.
3. No Power criteria: - The VANET node is equipped with a battery that is used as an infinite power supply for the communication and computation task
4. Time Management: - Safety message are the main goal of VANET. Message in VANET must be delivered to the nodes within the time limit so that a decision can be made by the node and perform action according.
5. Wireless Communication: - Data transmission is generally done by nodes. Nodes are connected and exchange their information via wireless communication

## Slide 30: Challenges of communication
Basic challenges
  Timeliness
  Throughput
Communication in vehicles: stresses...
  Robustness
  Cost
Communication across vehicles: also needs...
  Interoperability
  Reachability
  Security
  Privacy

## Slide 31: Cont…
The main challenges of the VANETs can be summarized as follows:
  Due to high mobility neighborhood location changes frequently-network Management.
  The unbounded network size.(channel load) Congestion and collision Control:
  Due to mobility signal power changes continuously.
  Environmental impact VANETs uses the electromagnetic waves for communication.
  Security as VANET provides the road safety applications which are life critical therefore security of these messages must be satisfied.

## Slide 32: V2V: goals and characteristics
Goals
  Safety
  Comfort
  Traffic efficiency
Safety applications have strict requirements on
  Reliability
  Delay

## Slide 33
Car-to-X Networking

## Slide 34: Vehicle-to-X (V2X) communication patterns
Vehicle-to-X (V2X),
Inter-Vehicle Communication (IVC),
Vehicular ad-hoc network (VANET),
…
Illustration: ETSI
… to infrastructure
… to vehicle
… to home

## Slide 35: Use Cases
Illustration: CVIS
Illustration: CVIS

## Slide 36: Taxonomy of Use Cases
Vehicle-to-X
Non-Safety
Safety
Adaptive Cruise Control
Comfort
Blind Spot Warning
Warning Messages
Electronic Brake Light
Traffic Information Systems
Optimal Speed Advisory
Situation Awareness
Contextual Information
Traffic Light Violation
Entertainment
Congestion, Accident Information

## Slide 37: Taxonomy of Use Cases
Non-Safety
Safety
Vehicle-to-X
Many messages
High data rate
Few messages
Small packet size
Low latency demands
Low reliability demands
High latency demands
High reliability demands

## Slide 38: Diversity of use cases
Application | Distance | Time | Recipient
Hazard warning | 250m | 10s | All
Location based service | 1..5km | Weeks | Subscribers
City wide alarm | 20km | Hours | All
Travel time information | 5km | Minutes | All
File sharing | 250m | Minutes (Index) Days (Content) | Subscribers (Index) Peers (Content)
Interactive Services | 1..5km | Minutes | Subscribers
[1] Bai, F. and Krishnamachari, B., "Exploiting the Wisdom of the Crowd: Localized, Distributed Information-Centric VANETs," IEEE Communications Magazine, vol. 48 (5), pp. 138-146, May 2010

## Slide 39: Diversity of requirements
Application | Latency | Reliability | # Vehicles | Area | Persistence
Information Query | ★ | ★ | ★★★ | ★★★ | 
Hazard Warning | ★★★ | ★★ | ★★ | ★★★ | 
ACC, el. Brake Light | ★★★ | ★★ | ★ | ★ | 
Cooperative Awareness | ★★ | ★★★ | ★ | ★ | ★
Intersection Assistance | ★★ | ★★★ | ★★ | ★★ | ★
Platooning | ★★★ | ★★★ | ★★ | ★ | ★
[1] T. L. Willke, P. Tientrakool, and N. F. Maxemchuk, "A Survey of Inter-Vehicle Communication Protocols and Their Applications," IEEE Communications Surveys and Tutorials, vol. 11 (2), pp. 3-20, 2009

## Slide 40: Motivation
1970s: bold ideas
  Very visionary, infrastructure-less solutions
  Unsupported by current technology
Early interest of government and industry
  working prototypes in: Japan CACS (1973–1979), Europe Prometheus (1986–1995), U.S. PATH (1986–1992)
  No commercial success
1980s: paradigm shift
  From complete highway automation ⇨ driver-advisory only
  Infrastructure-less ⇨ infrastructure-assisted
  chicken-and-egg type of standoff
New technology re-ignites interest
  latest-generation cellular communication ⇨ early “Car-to-X” systems
  e.g., On Star (1995), BMW Assist (1999), FleetBoard (2000), and TomTom HD Traffic (2007).
Sharp increase in computing power
  Supports fully-distributed, highly reactive ad hoc systems
[1] W. Zimdahl, “Guidelines and some developments for a new modular driver information system,” in 34th IEEE Vehicular Technology Conference (VTC1984), vol. 34., Pittsburgh, PA: IEEE, May 1984, pp. 178–182.

## Slide 41: Renewed interest of government and industry
Numerous field operational tests
  simTD (€ 69M), Aktiv (€ 60M), Smart Highway (€ 57M), Drive C2X (€ 19M), TeleFOT (€ 15M), SafeTrip (€ 10M), …
Dedicated spectrum in U.S., Europe, Asia
Illustration: FOT-NET Wiki
?

## Slide 42: Motivation
Traditional Network
  Connection: wired
  Nodes: non-moving
  Configuration: static
Mobile Ad Hoc Network (MANET)
  Connection: wireless
  Nodes: mobile
  Configuration: dynamic
  (Infrastructure: optional)
Vehicular Ad Hoc Network (VANET)
  Not: “MANET on wheels”
  Different topology dynamics, communication patterns, infrastructure, ...
[1] M. Scott Corson and Joseph Macker, "Mobile Ad hoc Networking (MANET): Routing Protocol Performance Issues and Evaluation Considerations,“ RFC 2501, January 1999

## Slide 43: Freeway ⇔ Urban
1D mobility
Bimodal connectivity
  Stable connection (vehicles on same lane)
  AND
  unstable connection (vehicles on opposite lane)
High speed
…
2D mobility
Bipolar connectivity
  Many neighbors (when standing)
  OR
  Few neighbors (when driving)
Obstacles
…

## Slide 44: Levels of infrastructure support
Pure ad hoc communication
Stationary Support Units (SSU)
  Radio-equipped autonomous computer
  Inexhaustible storage, energy supply
  Known position, high reliability
Roadside Units (RSU)
  SSU(System Synchronization Unit) plus…
  Ethernet NIC, UMTS radio(3G Universal Mobile Telecommunications System), ...
  Connected to other RSUs
Traffic Information Center (TIC)
  Central server connected to RSUs

## Slide 45: Infrastructure ⇔ No Infrastructure
Central coordination
  Resource management
  Security
High load on core network
Self organizing system
  Channel access
  Authentication
Low data rate
Source: AKTIV CoCar

## Slide 46: Convergence towards heterogeneous approaches
Same system needs to work in multiple environments
  Vehicle starts to drive in city with infrastructure support
  Continues driving on freeway (still with infrastructure support)
  Loses infrastructure support when turning onto local highway
  Finishes driving in city without infrastructure support

## Slide 47: Challenges of V2X communication
Communication
Highly varying channel conditions
Tightly limited channel capacity
Networking
Unidirectional Links (Broadcast, No Responce from Receiver)
Mobility
Multi-Radio / Multi-Network
But: predictable mobility
Security
No (or no reliable) uplink to central infrastructure
Highly dynamic topology
Heterogeneous equipment
Heterogeneous user base
Ensuring privacy
High congestion, contention, interference
Heterogeneous environment

## Slide 48: Technology

## Slide 49: Communication paradigms and media
Infrastructure-based
GSM 2G Cellular
Infrastructureless
Millimeter, Infrared, Visible
802.15.1 Bluetooth
802.15.4 ZigBee
DSRC / WAVE
UMTS 3G Cellular
LTE / WiMAX
4G Cell.
802.11 Wi-Fi
Broadcast
Short Range
Medium Range
FM Radio, DAB/DVB, …
Cellular
Wireless Communication Technologies
[1] Dar, K. et al., "Wireless Communication Technologies for ITS Applications," IEEE Communications Magazine, vol. 48 (5), pp. 156-162, May 2010

## Slide 50: Communication paradigms and media
Cellular and DSRC prove to be potential communication technologies enabling connected cars
The two major vehicular wireless communication technological standards:
  IEEE 802.11p (DSRC/WAVE)
  Cellular V2X (C-V2X)

## Slide 51: Communication Technologies
Notes: European Union
Cooperative Vehicles and Infrastructure Systems is in charge of traffic control systems and implements a variety of driver
routing systems based on hazardous conditions.
The main objectives of this trial are to develop standards for V2V and V2I communications,

## Slide 52: How does this work?
It is cooperative, dynamic and ad-hoc
Two different approaches, same network technology (IEEE 802.11p)
  US: Wireless Access in Vehicular Environments – WAVE – over Dedicated Short Range Communications – DSRC
  EU: ETSI TC ITS standards, using Geo-networking
Essentially: vehicles emit periodically or event-driven status information
  called Basic Safety Messages (BSM, US)
  and Cooperative Awareness Messages (CAM, EU)
  picture from the Internet

## Slide 53: IEEE 802.11p characteristics
Part of the full IEEE 802.11 (2800page) specification
  enhancements for use in Vehicles
Connect without BSS (BSS: stations with access point):
  no association, authentication
  just direct, ad-hoc messaging when in range
Support prioritizing of traffic: EDCA (from 802.11e)
Deal with high relative speeds of terminals
UTC-based timing reference for synchronizing time accurately
Channels in the 5.9 GHz range (~300m in free field, max 1000)

## Slide 54: US: WAVE/DSRC
  IEEE 802.11p standard
    A Dedicated Short Range Communication (DSRC) is proposed which is operating on 5.9GHz band and uses 802.11 access methods
    provides short range communication with low latency.
    add wireless access in vehicular environments (V2V, I2V Communications)
  IEEE 1609 standard
    family of standards that function in the middle layers of the protocol stack to flexibly support safety applications in VANETs .
  J2735 standard
    placed in the application layer
    It defines message sets, data frames and elements which are used for V2V and V2I safety exchanges
Notes: European Union
Cooperative Vehicles and Infrastructure Systems is in charge of traffic control systems and implements a variety of driver
routing systems based on hazardous conditions.
The main objectives of this trial are to develop standards for V2V and V2I communications,

## Slide 55: US: WAVE/DSRC
IEEE 1609 standardizes Wireless Access in Vehicular Environments over Dedicated Short Range Communication
  1609.1: resource management
  1609.2: security services
  1609.3: networking services (a.o. wave short message protocol)
    broadcasting of basic safety messages
    define channel number and power per message
  1609.4; multi-channel operation
SAE J2735
  defines the message content of WSMP

## Slide 56: Protocol Stack: IEEE 802.11p (DSRC/WAVE)

## Slide 57: Combining with Internet
WSMP
IP packet
Internet Apps
TCP/UDP
IPv6
PHY (IEEE 802.11p)
LLC/MAC (IEEE 802.11p with CSMA/CA)
P1609.4
WAVE Apps
  WAVE (Wireless Access in Vehicular Environment) standards:
  IEEE 802.11p standard and 1609.x standards
1609.x
(1,2,3)

## Slide 58: IEEE 802.11{a,b,g,n} for Car-to-X communication?
  Can’t be in infrastructure mode and ad hoc mode at the same time
  Switching time consuming
  Association time consuming
  No integral within-network security
  (Massively) shared spectrum (⇨ ISM)
  No integral QoS
  Multi-path effects reduce range and speed

## Slide 59: IEEE 802.11p
IEEE 802.11p
  PHY layer mostly identical to IEEE 802.11a
    Variant with OFDM and 16 QAM
    Higher demands on tolerances
    Reduction of inter symbol interference because of multi-path effects
      Double timing parameters
      Channel bandwidth down to 10 MHz (from 20 MHz)
      Throughput down to 3 ... 27 Mbit/s (from 6 ... 54 Mbit/s)
      Range up to 1000 m, speed up to 200 km/h
  MAC layer of IEEE 802.11a plus extensions
    Random MAC Address
    QoS (EDCA priority access, cf. IEEE 802.11e, ...)
    Multi-Frequency and Multi-Radio capabilities
    New Ad Hoc mode
    ...

## Slide 60: Differences between IEEE 802.11p and IEEE 802.11a

## Slide 61: Differences between IEEE 802.11p and IEEE 802.11a
Narrower bandwidth (10 MHz)
  Halves the occupied frequency space compared to 20 MHz in 802.11a
  You speak fewer words per second but more clearly,
  so the listener can catch them despite wind and echoes.
Carrier spacing halved
  The 802.11p signal uses a carrier spacing reduced by ½ compared to 802.11a.
Symbol length doubled
  Symbol time = 1 ÷ carrier spacing.
  Halving the spacing doubles the symbol duration (from 4 µs to 8 µs, plus guard interval), improving tolerance to multipath delay spread.
"Narrower bandwidth (10 MHz) →Carrier spacing halved →Symbol length doubled
Halves data rate-->doubles symbol time = improving tolerance to multipath delay spread.

## Slide 62: Differences between IEEE 802.11p and IEEE 802.11a
Carrier spacing halved
The 802.11p signal uses a carrier spacing reduced by ½ compared to 802.11a.
carrier spacing = bandwidth ÷ number of subcarriers.
Keeping 52 subcarriers but halving bandwidth from 20 MHz to 10 MHz halves the spacing (from 312.5 kHz to 156.25 kHz).

## Slide 63: Differences between IEEE 802.11p and IEEE 802.11a
Think of it like cars on a highway:
In 802.11a (blue), the lanes (carrier spacing) are wide apart, and cars are going very fast (short symbol time).
That’s fine on a smooth, straight road, but if there are bumps (signal reflections) or gusts of wind (Doppler shifts), you can easily lose control because everything happens so quickly.
In 802.11p (red), the lanes are closer together (smaller carrier spacing) and all cars drive slower (longer symbol time).
Because they’re moving slower, they have more reaction time if a bump or gust happens —
meaning the system can handle reflections and frequency shifts without “crashing” the communication.
Halves data rate-->doubles symbol time = improving tolerance to multipath delay spread.

## Slide 64: Classic IEEE 802.11
Classic IEEE 802.11 Basic Service Set (BSS)
  Divides networks into logical units
    Nodes belong to (exactly one) BSS
    Packets contain BSSID
    Nodes ignore packets from “foreign” BSSs
    Exception: Wildcard-BSSID (-1) for probes
    Ad hoc networks emulate infrastructure mode
  Joining a BSS
    Access Point sends beacon
    Authentication dialogue
    Association dialogue
    Node has joined BSS
BSS
SSID “A”
BSS
SSID “B”
BSS
SSID “C”

## Slide 65: IEEE 802.11p
New: 802.11 WAVE Mode
  Default mode of nodes in WAVE
  Nodes may always use Wildcard BSS in packets
  Nodes will always receive Wildcard BSS packets
  May join BSS and still use Wildcard BSS
BSS
SSID “A”
BSS
SSID “B”

## Slide 66: IEEE 802.11p
New: 802.11 WAVE BSS
  No strict separation between Host and Access Point (AP)
  Instead, loose classification according to:
    Equipment: Roadside Unit (RSU) / On-Board Unit (OBU)
    Role in data exchange: Provider (offers service) / User (uses service)
  No technical difference between Provider and User —no hardware difference.
  Provider sends On-Demand Beacon
    Analogous to standard 802.11-Beacon
    Beacon contains all information and parameters needed to join
  User configures lower layers accordingly
    Starts using provided service
    No additional exchange of data needed
  BSS membership now only implied
    There's no formal “join” process.
    Once a beacon is received and used, the User is considered part of the BSS.
    BSS continues to exist even after provider leaves

## Slide 67: IEEE 802.11 DCF
IEEE 802.11 Distributed Coordination Function (DCF)
  aka “Contention Period”
  Priority access via SIFS (ACK, CTS, ...) and DIFS (payload)
  Wait until medium has been free for duration of DIFS
  If medium busy, wait until idle, then wait DIFS plus random backoff time
Medium busy
TX starts
SIFS, PIFS, DIFS
Time slots in contention period

## Slide 68: IEEE 802.11 DCF
IEEE 802.11 Distributed Coordination Function (DCF)
  Backoff if
    Node is ready to send and channel becomes busy
    A higher priority queue (⇨ next slides) becomes ready to send
    Unicast transmission failed (no ACK)
    Transmission completed successfully
  Backoff: Random slot count from interval [0, CW]
  Decrement by one after channel was idle for one slot (only in contention period)
  In cases b) and c), double CW (but no larger than CWmax)
  In case d), set CW to CWmin

## Slide 69: IEEE 802.11p
QoS in 802.11p (HCF)
  cf. IEEE 802.11e EDCA
  DIFS ⇨ AIFS (Arbitration Inter-Frame Space)
    DCF ⇨ EDCA (Enhanced Distributed Channel Access)
  Classify user data into 4 ACs (Access Categories)
    AC0 (lowest priority)
    …
    AC3 (highest priority)
  Each ACs has different...
    CWmin, CWmax, AIFS, TXOP limit (max. continuous transmissions)
  Management data e.g, WAVE Service Advertisement (WSA), Timing synchronization) uses DIFS (not AIFS)

## Slide 70: IEEE 802.11p
QoS in 802.11p (HCF)
  Map 8 user priorities (Min:0 Max:7) ⇨ 4 access categories ⇨ 4 queues
  Queues compete independently for medium access
AC0
AC1
AC2
AC3
virtual collision

## Slide 71: IEEE 802.11p
QoS in 802.11p (HCF)
AC_VO → Priority (P):6-7 # Used for safety-critical messages (e.g., BSM) → (shortest AIFS, smallest contention window.)
AC_VI → Priority (P):4-5 # Non-critical but time-sensitive infotainment.
AC_BE → Priority (P):1-3 # Default for general data.
AC_BK → Priority (P):0 # Low-priority background updates.
IEEE 802.11e defines 8 possible priorities (0–7),
but EDCA only supports 4 queues in hardware:
  AC_VO (Voice)
  AC_VI (Video)
  AC_BE (Best Effort)
  AC_BK (Background)

## Slide 72: IEEE 802.11p
QoS in 802.11p (HCF)
  Parameterization
  Sample queue configuration
Parameter | Value
SlotTime | 13µs
SIFS | 32µs
CWmin | 15
CWmax | 1023
Bandwidth | 3 .. 27 mbit/s
Parameter | AC_BK | AC_BE | AC_VI | AC_VO
CWmin | CWmin | CWmin | [(CWmin+1)/2]-1 | [(CWmin+1)/4]-1
CWmax | CWmax | CWmax | CWmin | [(CWmin+1)/2]-1
AIFSn | 9 | 6 | 3 | 2

## Slide 73: Classical IEEE 802.11
After detecting the medium being idle for a duration of AIFS[AC] (Arbitration Interframe Space), backoff entity start down‐counting. AIFS is calculated as follow:
  AIFS[AC] = SIFS + AIFSN[AC]∙aSlotTime >= 2
Min and Max of the contention window are the other parameters dependent on AC.
QoS in 802.11p (HCF)
  Parameterization

## Slide 74: IEEE 802.11p
AC_VO
AC_VI
AC_BE
AC_BK
Channel Access
Backoff: 0
0
0
0

## Slide 75: IEEE 802.11p
AC_VO
AC_VI
AC_BE
AC_BK
Backoff: 0
0
0
0
Channel busy?
Start Contention
Wait for Idle
Channel Access

## Slide 76: IEEE 802.11p
AC_VO
AC_VI
AC_BE
AC_BK
0
0
0
Backoff 0?
Wait AIFS (SIFS + AIFSn * Slot len)
Wait for backoff = 0
Backoff: 0
Channel Access

## Slide 77: IEEE 802.11p
Backoff: 0
AC_VO
AC_VI
AC_BE
AC_BK
Backoff: 2
0
0
0
Transmission
Over
Post Transmit
Backoff
Channel Access

## Slide 78: IEEE 802.11p
2
AC_VO
AC_VI
AC_BE
AC_BK
Backoff: 2
0
0
0
AC_VI Queue ready to send… wait AIFS
Backoff
Ch becomes
busy
Channel Access

## Slide 79: IEEE 802.11p
Backoff: 2
2
1
AC_VO
AC_VI
AC_BE
AC_BK
Backoff: 1
0
0
Channel idle
Channel busy
[Slot time passed]
/Decrement Backoff
Channel state changes
Backoff: 0
0
Channel Access

## Slide 80: IEEE 802.11p
3
Backoff: 0
0
AC_VO
AC_VI
AC_BE
AC_BK
0
0
Queue ready to send
Internal Contention
Backoff
Higher priority queue ready
Channel Access

## Slide 81: IEEE 802.11p
QoS in WAVE
  mean waiting time for channel access, given sample configuration (and TXOP Limit=0 ⇨ single packet)
  when channel idle:
  when channel busy:
Figure Source: Eichler, S., "Performance evaluation of the IEEE 802.11p WAVE communication standard," Proceedings of 66th IEEE Vehicular Technology Conference (VTC2007-Fall), Baltimore, USA, October 2007, pp. 2199-2203
AC | CWmin | CWmax | AIFS | TXOP | tw (in μs)
0 | 15 | 1023 | 9 | 0 | 264
1 | 7 | 15 | 6 | 0 | 152
2 | 3 | 7 | 3 | 0 | 72
3 | 3 | 7 | 2 | 0 | 56

## Slide 82: UMTS/LTE vs. 802.11p
Pros of UMTS/LTE
  Easy provision of centralized services
  Quick dissemination of information in whole network
  Pre-deployed infrastructure
  Easy migration to (and integration into) smartphones
Cons of UMTS/LTE
  High short range latencies (might be too high for safety)
  Network needs further upgrades (smaller cells, multicast service)
  High dependence on network operator
  High load in core network, even for local communication

## Slide 83: UMTS/LTE vs. IEEE 802.11p
Pros of 802.11p/Ad hoc
  Smallest possible latency
  Can sustain operation without network operator / provider
  Network load highly localized
  Better privacy (⇨ later slides)
Cons of 802.11p/Ad hoc
  Needs gateway for provision of central services (e.g., RSU)
  No pre-deployed hardware, and hardware is still expensive
The solution?
  hybrid systems: deploy both technologies to vehicles and road, decide depending on application and infrastructure availability

## Slide 84: Higher Layer Standards for IEEE 802.11p
Channel management
  Dedicated frequency band at 5.9 GHz allocated to WAVE
    Exclusive for V2V und V2I communication
    No license cost, but strict rules
    1999: FCC reserves 7 channels of 10 MHz (“U.S. DSRC”)
      2 reserved channels, 1+4 channels for applications
    ETSI Europe reserves 5 channels of 10 MHz
[1] ETSI ES 202 663 V1.1.0 (2010-01) : Intelligent Transport Systems (ITS); European profile standard for the physical and medium access control layer of Intelligent Transport Systems operating in the 5 GHz frequency band
U.S. allocation | … | Critical Safety of Life | SCH | SCH | Control Channel (CCH) | SCH | SCH | Hi-Power Public Safety | …
European allocation |  | SCH | SCH | SCH | SCH | CCH | SCH | SCH | 
IEEE Channel |  | 172 | 174 | 176 | 178 | 180 | 182 | 184 | 
Center frequency |  | 5.860 GHz | 5.870 GHz | 5.880 GHz | 5.890 GHz | 5.900 GHz | 5.910 GHz | 5.920 GHz | 

## Slide 85: DSRC:: Channel Allocation (U.S. allocation)

## Slide 86: DSRC:: Channel Switching Timing
Safety Applications :
Primary Message Type: BSM (Basic Safety Message) – Periodically broadcast vehicle status (position, speed, heading).
Channel Used: Control Channel (CCH) or Safety Channel (SfCH)

## Slide 87: Message Type and Channel Used
Safety Applications :
Primary Message Type: BSM (Basic Safety Message) – Periodically broadcast vehicle status (position, speed, heading).
Channel Used: Control Channel (CCH) or Safety Channel (SfCH)
Non-Safety Applications :
Primary Message Types:
  WSA (WAVE Service Advertisement) – Broadcasts the availability of a service on a specific channel.
  WSM (WAVE Short Message) – Payload message sent after WSA received/accepted.
Channel Used: Service Channels (SCHs) (e.g., 5.860 GHz–5.880 GHz, 5.910 GHz–5.920 GHz)

## Slide 88: Higher Layer Standards for IEEE 802.11p
Need for higher layer standards
  Unified message format
  Unified interfaces to application layer
U.S.
  IEEE 1609.*
  WAVE („Wireless Access in Vehicular Environments“)
Europe
  ETSI
  ITS G5 (“Intelligent Transportation Systems”)

## Slide 89: IEEE 1609.* upper layers (building on IEEE 802.11p)
IEEE 1609.2: Security
IEEE 1609.3: Network services
IEEE 1609.4: Channel mgmt.
IEEE 1609.11: Application “electronic payment”
[1] Jiang, D. and Delgrossi, L., "IEEE 802.11p: Towards an international standard for wireless access in vehicular environments," Proceedings of 67th IEEE Vehicular Technology Conference (VTC2008-Spring), Marina Bay, Singapore, May 2008
[2] Uzcátegui, Roberto A. and Acosta-Marum, Guillermo, "WAVE: A Tutorial," IEEE Communications Magazine, vol. 47 (5), pp. 126-133, May 2009
TCP / UDP
WAVE PHY
Channel Coordination, WAVE MAC
IPv6
WSMP
Management
Security
LLC
802.11p
1609.4
1609.3
1609.2
WAVE PHY

## Slide 90: IEEE 1609
Channel management
  WAVE allows for both single radio devices & multi radio devices
  Dedicated Control Channel (CCH) for mgmt and safety messages ⇨ single radio devices need to periodically listen to CCH
  Time slots
    Synchronization envisioned via GPS receiver clock
    Standard value: 100ms sync interval (with 50ms on CCH)
    Short guard interval at start of time slot
      During guard, medium is considered busy (⇨ backoff)
CCH interval
CCH interval
“SCH” interval
“SCH” interval
[1] IEEE Vehicular Technology Society, "IEEE 1609.4 (Multi-channel Operation)," IEEE Std, November, 2006
t = n × 1s

## Slide 91: IEEE 1609
Packet transmission
  Sort into AC queue, based on WSMP (or IPv6) EtherType field, destination channel, and user priority
  Switch to desired channel, setup PHY power and data rate
  Start medium access
CCH
SCH
AC0
AC1
AC2
AC3
virt. Collision
AC0
AC1
AC2
AC3
virt. Collision
Channel Router
Channel selection and setup
Channel access

## Slide 92: IEEE 1609
Channel management
  Control Channel (CCH):
    Default channel upon initialization
    BSM(Basic Safety Message), WAVE service advertisements (WSA)
    Channel parameters take fixed values
  Service Channel (SCH):
    Only after joining WAVE BSS
    WAVE short messages (WSM), IP data traffic (IPv6)
    Channel parameters can be changed as needed

## Slide 93: IEEE 1609
WAVE service advertisement (WSA)
  Broadcast on Control Channel (CCH)
  Identifies WAVE BSSs on Service Channels (SCHs)
  Can be sent at arbitrary times, by arbitrary nodes
  Only possibility to make others aware of data being sent on SCHs, as well as the required channel parameters to decode them
Node A
Node B
WSA (on CCH)
Data (on S-CH)
Data (on S-CH)

## Slide 94: Loss Model

## Slide 95: Loss Model::Line Of Sight
The term LOS path is referred the situation where we have visual line of sight contact between the transmitting antenna and the receiving antenna.
The Ricean distribution can be used for modeling small-scale fading

## Slide 96: Loss Model:: Non-Line Of Sight
For the N-LOS path it is found that the amplitude of the received signal due to fading obeys Rayleigh fading distribution and the delay spreads were several times greater than that for the LOS.

## Slide 97: Vehicular Networking
Book design © 2014 Cambridge University Press